## Slide 1
1
Subject, problem, issues (Context) (Goal)
Data exploration (volume, architecture)
  identification long.mode, MAC
  (streamlit) dataframes
Data visualization
  - (streamlit) distribution of the expl. variables + correlation heatmap
  - (streamlit) identified long. mode + neighboring modes
Pre-processing
  slot classes
  NRDD
  - Result overview
Long .frequencies Modelling
  (streamlit) Trained models and results, tuned model
  (streamlit) Best & worst predictions
  (streamlit) Filtered data
Link results with the business issue, Next Steps & Conclusion
Conclusion & Outlook

## Slide 2: Francois Brouet – sep24_continuous_ds

## Slide 3
Presentation
Next steps / Conclusion
07
Modelling
06
Result overview
05
Pre-processing
04
Data visualization
03
Data exploration
02
Context
01
Streamlit
Streamlit
Notes: Good afternoon, I am pleased to present you today the results of my Data Science Project
The presentation will be divided in the following sections: I will show you some elements in the slides and then will switch to streamlit at some points of the presentation

## Slide 4: Context
Concept of the ultrasonic welding:
vibration energy  welding part
energy  heat
force  new connection
Ultrasonic sonotrode
longitudinal mode used to drive the vibration
Requirements:
  frequency ~ 20 kHz
  longitudinal mode isolated
  uniform output displacements
Notes: Principle of US-Welding
Mechanical vibrations transfer the kinetic energy into a welding part
This energy is transformed into heat by the surface friction
The material starts to melt
The material is compressed by a mechanical force (parallel to melting)
A new homogeneous connection is created
Sonotrode:
is in contact with the welding part
has many vibrating modes (each mode has an eigenfrequency and an eigenshape)
longitudinal mode is used
these modal properties are calculated with FEM software (ANSYS)
Requirements
  Longitudinal mode‘s frequency should be close to 20 kHz (driving frequency)
  Longitudinal mode should be isolated from other modes
  Longitudinal mode‘s displacements should be as uniform as possible over the welding surface

## Slide 5: Goal
  Main goal: Prediction of the FEM results from the sonotrode geometry
  3 predictions:
  longitudinal frequency
  frequencies of all modes
  uniformity of the output displacements
  Geometry: 23 parameters
  (dim_x) × (dim_z): output surface
  (dim_y): length
  …
Notes: Goal of this project was to predict the results of FEM simulations (modal properties) without running them
Simulations of complex geometries are computer-intensive  one iteration can take up to an hour
FEM results splitted in 3 subgoals (different target variables)
- Prediction of the longitudinal mode’s frequency
- Prediction of the frequency of all other modes: particulary near the longitudinal mode (ex: 5 modes below and 5 modes above).
- Prediction of the uniformity of the displacements (as a number), instead of all displacement values
Geometry described by 23 parameters
dim_x / dim_z welding (output) surface, usually fixed by the welding part
dim_y: oscillation length, typical feature to tune the longitudinal frequency
here: 4 slots and 2 slots in both directions
other dimensions: free, used to optimize the modal properties of the sonotrode

## Slide 6: Data exploration
  MAC (Modal Assurance Criterion)
    comparison: mode shapes with reference longitudinal mode shape
    0 no correspondance
    1 full correspondance
  Identification of the longitudinal mode
  Long. mode: highest MAC value
  8000 design points (DP) = geometries
  CSV files
Notes: Before taking a look at the dataset, I present right away 2 important notions:
the MAC value is an indicator, comparing the calculated mode shapes with a reference shape, chosen as an ideal long. mode shape
The mode shapes are vectors of displacements (for a matter of simplicity, we take only the displacements of the nodes located at the input and output surfaces)
the MAC value is bounded between 0 (no correspondance with the long. mode shape) and 1 (equals the longitudinal mode shape)
the MAC value is directly calculated in the FEM program when the simulation is complete
When a simulation is complete and all modes are calculated, the long. mode is found by comparing the MAC value of every mode.
The mode with the highest value is marked as the long. mode. The mode number can change between 2 geometries.
A design point represents a unique geometry as a 23-dimensional vector. Before the project, the DP are randomly picked inside a parameter space, that I defined to keep a valid sonotrode geometry.
There are about 8000 DP. The data was stored in CSV files written by the FEM program ANSYS.
During the step of data collection, I imported the 24,000 CSV files into 4 dataframes, that we will see right now in streamlit

## Slide 7: Data exploration
  (Streamlit)
Notes: * Exploration of the data
4 dataframes:
- parameters (concatenation of 3 groups of columns)
(columns)
* 1st part contains the geometric parameters
* next columns contain the identification features of the long mode
* last part contains the additional features (see later: slot class, uniformity criterion, frequency isolation)
(rows)
DP (here only 100)
- modes: all combinations of DP and mode numbers
Start with DP 1001, all modes from position 25 to position 100
For each mode we get some properties: frequency, MAC
- nodes: all combinations of DP and nodes
Node coordinates XYZ located on the output surface
- displacements: largest dataframe
combination of DP / nodes / modes 25 to 100
Let‘s switch to the
* Data visualization
The distribution of the explanatory variables are represented: the geometric parameters have been randomly generated according a normal distribution
 boxplot is symmetrical, median in the center, whiskers are on equal length on both sides
slot_x_distance and slot_z_distance have a skew distribution  they are depending on the variable number of slots
Example of DP 1001:
You see in the dataframe extract the geometric parameters
Identified long. mode is mode 77, why?
- In the mode list:
MAC value 0.92 maximal for mode 77
Long. frequency is frequency of mode 77: 19218
Delta frequency to the next mode is only 61 Hz
Let‘s see the displacements for these 3 modes
Displacements of mode 77 are not perfectly uniform (anyway of the same sign)

## Slide 8: Pre-processing
  Slot classes
  NRDD
  Norm of the Relative Displacement Deviation
depth (z)
width (x)
displacement of the node n
average of all displacements
number of nodes (output surface)
Notes: I added new features to the dataset
The sonotrode needs slots in both directions for acoustical reasons and the number of slots is variable. During the generation of the design points, I used 4 combinations of slot distributions.
The width (highest dimension) needs more slots than the depth.
The numbers of slots in both directions are categorical and building a class with 4 values
The prediction of the output displacements themselves did not turned out accurate. Since the 3rd goal is to predict only the uniformity, I introduced a new metric to evaluate the uniformity of the displacements.
The Norm of the Relative Displacement Deviation (called NRDD) is obtained:
by taking the relative difference of the displacements to the average
the deviations are squared and summed up for all nodes
the root value gives the NRDD value

## Slide 9: Pre-processing
  NRDD = 0 perfect uniform displacements
  NRDD > 10 poor uniformity
(NRDD = 1.3)
Notes: A low value of NRDD corresponds to uniform displacements and high values to poor uniformities (the deviations are important)
As an example, you see on the left the DP with the most uniform displacements, NRDD = 1.3
The graph on the right shows the correlation between the MAC values and the new metric NRDD
You will probably ask, why didn‘t I take the MAC value as target variable. The reason is that the models performed slightly better with the NRDD than with the MAC value directly.
So I decided to go on in that direction.

## Slide 10: Result overview
Target variable(s) | Best estimator | Final R² score | Mean Absolute Error
Frequency of the longitudinal mode | LightGBM | 0.997 | 21 Hz
All frequencies | LightGBM | 0.998 | 98 Hz
Displacements of the longitudinal mode | Dense Neural Network | 0.855 | 
Notes: I won‘t present all the models tested in that work but you see in the overview table the best results achieved for the 3 targets
For the rest of the presentation, we will focus in Streamlit on the longitudinal frequencies:
the target is a single value (contrary to all frequencies and displacements)
the score and the error are easy to interpret
I chose the R² score as a metric because:
- it‘s the default metric for the LightGBM regressor
- it‘s a universal + absolute metric that does not require any reference point

## Slide 11: Modelling
  (Streamlit)
Notes: I chose as the base model the regressor Light Gradient Boosting Machine because:
- quick & accurate
- can handle large datasets
Here are the results of the base + tuned models
- R² score
- MAE (arithmetic average of the abs. error) of 45 Hz
In the plots, you can see:
(left) the predicted values = f (real values)
(right) the residuals calculated as difference (Prediction – Real)
# (selectbox)
Then I tuned the hyperparameters with a Bayesian approach.
MAE sinked to 28 Hz, compared to 45 Hz for the base model
# (checkbox) Worst prediction
Let‘s have a closer look at the worst prediction to understand why the model was less accurate:
- Absolute error 237 Hz
- long. mode = 57
we observe that the MAC value of modes 55 + 57 are quite similar and significantly below 1
particular case: both modes have a very similar shape (as we see in the displacements plots) the identification is not obvious
# (checkbox) Scatterplot Res = f (MAC) shows that the residuals are smaller for well identified modes
# (selectbox)
Finally I decided to exclude from the training all the DP with poor MAC values (limit set at 0.75)  keep still 85% of the dataset
This filtering of the data set helped the model and improved significantly the accuracy of the predictions
 MAE reduced to 21 Hz, which is very good (0.1 % of the working frequency)

## Slide 12: Next steps & Conclusion
  1) Deployment of the models
  CAD Interface
  Geometry description
  2) Optimal geometry(ies)
  Optimizer
  Range of parameters
Thank you for your attention!
Notes: I am done with the results‘s presentation and would like to mention the next steps:
- to deploy the model in the production we will need
* a mask to enter the different parameters of the geometry
* an interface with the CAD program, so that the engineer gets a quick estimation of the modal properties before the simulation
* find a better way to describe the geometry with new variables (instead of dimensions)?
- to find the optimal geometry (or geometries) an optimizer will be required
* the optimizer will work with the predictions, can navigate in the parameter space much faster to find the optimas
* the range of parameters has to be defined before, or can be automatically proposed by the optimizer
Thank you for your attention. Now I would be happy to hear your comments and answer your questions

## Slide 14: Introduction
01