## Slide 1: Francois Brouet – sep24_continuous_ds

## Slide 2
2
Subject, problem, issues
Data (volume, architecture)
Data visualization
Pre-processing
Long .frequencies: Trained models and results, best model
Long. displacements: Trained models and results, best model
Link results with the business issue
Criticism and outlook
20 min presentation
10 questions

## Slide 3: Introduction
01

## Slide 4: Context
Concept of the ultrasonic welding:
convert the vibration energy to the welding parts
energy transformed in heat by friction
with mechanical force  new connection
Ultrasonic sonotrode
longitudinal mode used to drive the vibration
must meet requirements:
  frequency ~ 20 kHz
  longitudinal mode isolated
  uniform displacements at the output
Notes: US-Welding
Mechanical vibrations transfer the kinetic energy into a part
This energy is transformed in heat by the surface friction
The material starts to melt
The material is compressed by a mechaniical force (parallel to melting)
A new homogeneous connection is created
Sonotrode:
is in contact with the welding part
has many vibrating modes (each mode has a eigenfrequency and a eigenshape)
longitudinal mode is used
Simulation with FEM software (ANSYS)
Requirements
  Longitudinal mode‘s frequency should be close to 20 kHz (driving frequency)
  Longitudinal mode should be isolated from other modes
  Longitudinal mode‘s displacements should be as uniform as possible over the welding surface

## Slide 5: Goal
  Main goal: Prediction of the FEM results from the sonotrode geometry
  3 predictions:
  longitudinal frequency
  frequencies of all modes
  uniformity of the output displacements
  Geometry: 23 parameters
  (dim_x) × (dim_z): output surface
  (dim_y): length
  …
Notes: Goal of this project was to predict the results of FEM simulations (modal properties) without running them
Simulations of complex geometries are computer-intensive  one iteration can take up to an hour
FEM results splitted in 3 subgoals (different target variables)
- Prediction of the longitudinal mode’s frequency (or “long. frequency”)
- Prediction of the frequency of all other modes: Focus near the longitudinal mode (ex: 5 modes below and 5 modes above).
- Prediction of the uniformity of the displacements (as a number), instead of all displacement values
Each subgoal:
visualization
parameter influences
modeling
result interpretation
Geometry
dim_x / dim_z welding (output) surface, usually fixed by the welding part
dim_y: oscillation length, important feature to tune the longitudinal frequency
here: 4 slots and 2 slots in both directions
other dimensions: free, used to optimize the modal properties

## Slide 6: Preprocessing
  Identification of the longitudinal mode
  Criterion NRDD
  (Data visualization Streamlit)
    NRDD: examples good/bad + distribution

## Slide 10
Tuning of the sonotrode geometry
The output surface is mostly defined by the welding part and can not be changed
The rest can be used to optimize the modal properties (tuning)
  Typically the length tunes the frequency
  Other parameters
    a (slot position)
    b (slot length)
    …

## Slide 11: Project
03

## Slide 12
Goal of the project: Create a model to predict FEM results
Model can be trained with FEM calculations
Design point can be chosen by the model
One design point ~ 1 minute
Predict FEM results with calculation
Combine prediction with optimization (optional goal)

## Slide 13
Post-processing script in ANSYS:
Identifies the longitudinal mode and its frequency (Global file for all design points)
Exports result data (One file for each design point):
  List of modes and frequencies
  List of node coordinates of the welding surface
  List of node displacements of the welding surface

## Slide 14
Example: Impact of the slots on modal frequencies
a: slot position
b: slot length

## Slide 16
Agenda
Thema 10
10
Thema 09
09
Thema 08
08
Thema 07
07
Thema 06
06
Thema 05
05
Thema 04
04
Thema 03
03
Thema 02
02
Thema 01
01
Ein- / Ausblenden von Agenda Themen
Entfernen bzw. hinzufügen weiterer Themen:
Start > Abschnitt „Bearbeiten“ > Markieren > Auswahlbereich
Dann erscheint rechts das Fenster Auswahl. Hier lassen sich einzelne Objekte aus- bzw. einblenden (klicken auf das „Augen-Symbol).